## Slide 1
ES 6350:2018
Safety and performance requirement for open resistor Electric cook stove

## Slide 2
Scope
This Ethiopian standard covers
constructional,
electrical and
physical requirements for household and
similar use open Resistor Electric heated
Cook Stove,
rated voltage being not more than 250 V for
single phase appliances connected between
phase and neutral.

## Slide 3
General requirements
The electric stove plate shall be made from clay, gypsum and
ceramic material or other materials having similar properties
The thickness of plate for flat type shall be uniform.
The slot depth and slot pitch shall be uniform throughout the plate.
Terminal connector shall be made of heat resistant material.
The accessible metal parts of electric stove shall be connected to
earthling terminal/contact for protection against electric shock..
Connecting wire (Amharic: woraj) between the heating element and
the terminal connector shall be enclosed with high heat resistive
insulator.

## Slide 4
    The wire between the terminal connector and
    the switch shall be heat resistant or enclosed
    with heat resistive material.
    Each cooking plate shall be equipped with a
    switch
    All legs of electric stove shall have uniform
    height
    Electric stove shall have safe handling
Con’d…….

## Slide 5
  Switch
  The switch shall be thermostat switch With user selectable
  range.
  Switch shall be protected against heat and / or liquid.
  Power cable
    The electric stove power cable quality shall comply with ES
    IEC 60227, rubber insulated cables rated voltage up to and
    including 450/750V.
    The power cable size shall withstand the current carrying
    capacity and comply with ES IEC 60287
    The minimum power cable length shall be not less than 1.5
    meter from the switch
Specific requirements

## Slide 6
  Plug
    The plug of electric stove shall comply with ES IEC 60906-1, plugs and
    socket outlets for household and similar purposes
  Cable entrances (grommet)
    Cable entrance shall be made of rubber, free from sharp edge and tightly
    fixed to the body
  Protection against electric shock
    All accessible metal parts shall be connected to an earthling terminal or
    contact reliably
  Clamp
    The stove power cable shall be fixed to the stove body with appropriate
    clamp.
  External Finish (Body)
    The external finish used on metal components shall be of heat and
    moisture resisting nature and shall not be adversely affected by variation
    in temperature occurring under normal operating conditions.
Con’d…….

## Slide 7
Body temperature
    Bottom temperature of the stove shall be 290 °c
    side temperature of the stove shall be 74°c
  Plate
    The width and depth of the slot shall
      Tightly hold the resistance wire in the slot with
      enough clearance from the top surface of the plate.
      Hold the resistor wire in place during normal
      operation and under idle condition in up-right
      position.
    A bowel type electric stove shall not have a hole at the
    center.
Contd…….

## Slide 8: Con’d
  Resistor Wire
    Electric stove resistor shall comply with ES 7938
Safety
The safety requirement for electric Cook stove shall comply with ES IEC 60335- 2-6 when ever applicable

## Slide 9
Thermal efficiency will be discussed in MEPS
and labeling

## Slide 10
Constructional requirements
The frame and enclosure of an appliance shall be of
substantial angle iron and sheet metal or of reinforced
sheet metal or of cast iron or other acceptable
construction and shall be sufficiently rigid and robust
to withstand, without deformation, the stresses
applied during installation, transportation, and
general usage of the appliance.
Contd…….

## Slide 11
Marking
In addition to the requirements in ES OIML R79:2013, each
package shall be legibly and indelibly marked with the
following:
a) Product name
b) Trade name
c) Address
d) Rated Voltage
e) Rated Power
f) Thermal efficiency
g) Warranty

## Slide 12
Thank You